## Slide 1
Yu-Lin Wei,
Sheng Shen, Daguan Chen, Zhijian Yang,
Voice Localization using Nearby Wall Reflections
Romit Roy Choudhury
Notes: Hello everyone. My name is Yu-Lin Wei from University of Illinois, Urbana Champaign. Today, I’m going to present our work Voice Localization using Nearby Wall Reflections.

## Slide 2
AoA (Angle of Arrival) = Angle in which a signal arrives
Notes: Our work focuses on solving the angle of arrival (AoA) problem.
The problem formulation is simple: if we have a microphone array,<br> how can we estimate the angle in which a signal arrives.<br>
This technique is widely adapted in various products like smart speakers, conference microphone, and directional antenna,

## Slide 3
Many variants of the problem … many AoA Algorithms
Delay-Sum
GCC-PHAT
MUSIC
ESPRIT
JADE
Notes: AoA is an important and well-researched problem. So there are many variants…
And also many excellent works solving this problem like GCC-PHAT, MUSIC, etc.

## Slide 4
Delay-Sum
GCC-PHAT
MUSIC
ESPRIT
JADE
Many variants of the problem … many AoA Algorithms
But still an open problem for MULTI-ECHO environment
Notes: However, AoA is still an open problem under some conditions. In this work, we are solving this problem considering many echoes in the environment

## Slide 5
1. A new AoA algorithm
2. Application: voice localization
This paper
Notes: In this talk, I’ll first present a new AoA algorithm, and later show how it could be used in an indoor localization scenario.

## Slide 6
What makes the problem challenging?
Notes: Let’s first see what makes AoA challenging? We have a microphone array as the receiver

## Slide 7
What makes the problem challenging?
1
N
# of sources
Notes: And we might have different number of sources. Either single source or N>1 sources

## Slide 8
What makes the problem challenging?
1
N
K
# of sources
# of echoes modeled
1
Notes: And each of them might produce one, or K more than 1 echoes

## Slide 9
What makes the problem challenging?
French
German
Latin
1
N
K
Source signals are unknown!
# of sources
# of echoes modeled
1
Notes: Moreover, the source signals are unknown

## Slide 10
French
German
Latin
What makes the problem challenging?
1
N
K
Goal: separate all N x K signal AoAs.
# of sources
# of echoes modeled
Holy Grail
(Very challenging)
1
Notes: And the goal is to separate the received signals, and estimate all N times K signal AoAs

## Slide 11
Existing solutions have made significant progress …
1
K
# of sources
# of echoes modeled
French
German
Latin
N
Holy Grail
(Very challenging)
1

## Slide 12
Existing solutions have made significant progress …
1
K
MUSIC
(Source uncorrelated)
# of sources
# of echoes modeled
French
German
Latin
Assumes signals are un-correlated
N
Holy Grail
(Very challenging)
1
Notes: For example, MUSIC algorithm can estimate the AoA of many source signals. <br> But it assumes all the signals are uncorrelated

## Slide 13
Existing solutions have made significant progress …
1
1
K
GCC-PHAT
MUSIC
(Line-of-Sight AoA)
# of sources
# of echoes modeled
French
German
Latin
Only estimate the Line-of-Sight AoA
(Source uncorrelated)
N
Holy Grail
(Very challenging)
Notes: GCC algorithm can estimate the direct path AoA quite well even if there are many echoes. <br>
But it can only estimate the direct path

## Slide 14
This paper: Voice Localizaion (VoLoc)
# of sources
1
# of echoes modeled
K
GCC-PHAT
MUSIC
VoLoc
French
German
Latin
Estimating multiple, fully correlated echoes
N
Holy Grail
(Very challenging)
(Line-of-Sight AoA)
1
(Source uncorrelated)
Notes: Our work, VoLoc, target to estimate all the AoAs of the echoes, in other words, we want to model all mutiple fully correlated echoes.
Fully correlated because these echoes are from a same source.

## Slide 15: Opportunities on AoA
Notes: To show how we separate the direct path from the reflected signal, let’s first zoom in to how conventional AoA algorithms work, and we can find opportunities inside.

## Slide 16
Delayed by
ΔT and AoA: 1-to-1 mapping
A simple correlation can find , hence AoA
Delayed by
Conventional AoA algorithm
Notes: How can we estimate the AoA using the microphone array?
Here we give an example of three microphone, and they are separated with same distance D
When the signal comes from an AoA theta, the left microphone first received the signal, and then the middle microphone after delta T seconds.
This is because the signal needs to travel a additional distance delta d, to arrive at the middle microphone.
And similarly, it arrives at the right microphone after another delta t seconds.
From geometry, we can see that both delta d and delta t is decided by the AoA theta, or we can say, the delta t and AoA is a one to one mapping
So we can use a simple correlation to find the signal delays between microphone, and infer the AoA

## Slide 17
With (infinite number of) echoes … ΔT’s are getting mixed
Impossible to decouple each ΔT from the mixture
Conventional AoA algorithm
Notes: But what if there are many paths from different direction? In this case each path will have different AoA, and hence different delta T.
These signal delay are getting mixed, and it’s nearly impossible to decouple each delta t if we don’t know the source signal

## Slide 18: Key opportunity – Human speech has many pauses
“Alexa, what time is it?”
Time (second)
Notes: So we’re introducing out key opportunity – human speech has many pauses, so we can leverage the time of each after each pause.
As shown in the red circle here. Right after the pause, the signal is not polluted by previous echoes because previous window is silence.

## Slide 19
ABCDEFG …
Voice Samples
Pause opportunity
Notes: Let’s zoom in to the voice signal, we denote the command as ABCDEFG and so on in time domain.
And there’s no voice before symbol A.

## Slide 20
A B C …
A B C …
A B C …
a b c …
a b c …
a b c …
Path #2 (1st Echo)
Path #3 (2nd Echo)
Path #1 (Direct Path)
a b c …
a b c …
a b c …
Pause opportunity
Notes: Let’s say there are 3 paths from the user to the microphone.
Microphone will receive the capital ABC from the direct path, and lower-case abc from the second path.
After a while, the third path comes as underscore abc

## Slide 21
A B C D E F G H I J K L M N ⋮
Time
A B C D E F G H I J K L ⋮
A B C D E F G H I J ⋮
Notes: If we plot the received signal on the timeline, we can see that, the signal first arrives at the left microphone first, and then the middle one after delta T seconds.
And then the right one.

## Slide 22
A B C D E F G H I J K L M N ⋮
Time
A B C D E F G H I J K L ⋮
A B C D E F G H I J ⋮
: Path #1
Slope:
Notes: This slope is decided by the direct path AoA. For example, here we can see the signal comes from the left-hand side because it arrives at the left microphone earlier.

## Slide 23
A B C D E F G H I J K L M N ⋮
Time
a b c d e ⋮
: Path #2
a b ⋮
A B C D E F G H I J K L ⋮
a b c d e f
⋮
a b ⋮
A B C D E F G H I J ⋮
a b c d e f
g ⋮
a b ⋮
: Path #1
: Path #3
Notes: The second path will arrive later. It’s reflected by the wall, so the path is longer. Denoted as the blue lower case abc here Also we’ll see a slope of the blue signal here, and this slope is decided by the second path AoA. In this figure, we can see that the second path comes from right hand side. And similarly we can see how the third path joins.

## Slide 24
A B C D E F G H I J K L M N ⋮
a b c d e ⋮
: Path #2
a b ⋮
A B C D E F G H I J K L ⋮
a b c d e f
⋮
a b ⋮
A B C D E F G H I J ⋮
a b c d e f
g ⋮
a b ⋮
Compute
: Path #1
: Path #3
Compute
Compute
Time
Notes: Here we can see that, before the first blue symbol, or the second path signal joins, the received signal is only affected by the direct path.
So we can use this segment to compute the direct path AoA. And before the green third path joins, this segment is only composed of direct path and second path. So we can use this segment to compute the second AoA, and so on. So after pauses in the speech, we see that the direct path, second path are joining one by one.
This gives us the chance to solve the AoA of the these paths one by one.

## Slide 25: Iterative Align and Cancel (IAC) algorithm
Notes: Here, I’m going to introduce our core algorithm: iterative align and cancel. This algorithm takes the received signal as the input and output the AoA of each path.

## Slide 26
A
B
C
D
E
F
…
A
B
C
D
…
Align
…
A
B
C
D
E
…
A
B
C
D
E
Cancel Path 1
-
-
-
-
-
-
-
Raw Signal
Aligned Signal
Residue
Find that minimizes residue
IAC step 1: Compute
Notes: Solving the direct path AoA is easy. This part is same with the conventional AoA algorithm that we just mentioned.With microphone pair (i, j), we find the delta T1 delay between microphones. If we find the correct delay, signals from two microphones will be identical, so we subtract one from another and the residue will be zero.
The delay delta T1 and AoA is an 1-to-1 mapping, so we can estimate the direct path AoA correctly.

## Slide 27
A
B
C
D
E
F
…
Raw Signal
G
H
I
J
L
M
K
a
b
c
d
e
f
…
A
B
C
D
E
F
G
H
I
J
K
…
a
b
c
d
e
f
…
g
Let’s first assume we know and see what can we get
IAC step 2: Compute
Notes: After computing the AoA1, Next let’s see how do we compute the AoA of the second path.
This is much harder, because now the microphone recording is the summation of both the direct path, the red signal, and the second path, the blue signal.
Let’s first assume we know the AoA2, and thus we know the delta T2, and what equations are there.

## Slide 28
A
B
C
D
E
F
…
Raw Signal
G
H
I
J
L
M
K
a
b
c
d
e
f
…
A
B
C
D
E
F
G
H
I
J
K
…
a
b
c
d
e
f
…
g
Residue
A
B
C
D
E
F
…
G
H
I
J
L
M
K
a
b
c
d
e
f
…
A
B
C
D
E
F
G
H
I
J
K
a
b
c
d
e
f
g
…
L
M
e
f
…
Aligned Signal
Cancel Path 1
-a
-b
-c
a-d
b-e
c-f
d-g
…
( differential of source signal)
Align
IAC step 2: Compute
Notes: In the first step, we align the microphone signal based on the first AoA, or delta T1. In this case, the red signal will be cancelled.
And let’s see what’s the residue? Of course the residue is all from second path, the blue part.
And we can see that now the second path is shifted by delta T1 + delta T2, so after subtract, we’ll get the time domain signal –a, -b, -c, a-d, and so on…, as the residue.

## Slide 29
Residue
A
B
C
D
E
F
…
G
H
I
J
L
M
K
a
b
c
d
e
f
…
A
B
C
D
E
F
G
H
I
J
a
b
c
d
e
f
…
…
Align
Aligned Signal
Cancel Path 2
A
B
C
D-A
E-B
F-C
G-D
…
( differential of source signal)
A
B
C
D
E
F
…
Raw Signal
G
H
I
J
L
M
K
a
b
c
d
e
f
…
A
B
C
D
E
F
G
H
I
J
K
…
a
b
c
d
e
f
…
g
IAC step 2: Compute
Notes: On the other hand, if we do not align the signals with delta T1, instead, we align using delta T2 and cancel the blue path.
The residual, of course, will now be the red direct path signals, with the same delta T1 + delta T2 shift.
Here it’s A, B, C, D-A, etc.

## Slide 30
A
B
C
D
E
F
…
Raw Signal
G
H
I
J
L
M
K
a
b
c
d
e
f
…
A
B
C
D
E
F
G
H
I
J
K
…
a
b
c
d
e
f
…
g
Align and Cancel
Align and Cancel
A
B
C
D-A
E-B
F-C
G-D
…
Residues
( differential of source signal)
-
-
-
-
-
-
-
2nd Path’s Shift () & Scale ()
Final Residue
-a
-b
-c
a-d
b-e
c-f
d-g
…
Find three variables, (1) , (2) 2ndpath’s time shift , (3) scale , that minimize final cancellation residue
IAC step 2: Compute
Notes: If we compare these two residuals, we’ll find that these residual array is linear dependent. We can shift the upper blue signal, multiply it with a scaler alpha, and it will become this lower red signal.The scaler is the amplitude ratio of the direct path and the second path.So if we can shift and scale the blue residue, and cancels the red residue vector.We can claim that we find the correct AoA2, or delta T2.This concludes the second step of IAC algorithm: find 3 variables, AoA2, time shift, and scale, that minimize the cancellation residue.

## Slide 31
Final Residue
2nd path’s time shift
2nd path’s scale 𝛼
But what happens with 3rd, 4th, and K incoming paths?
Objective Function is not Convex, but manageable …
Notes: The objective function is not convex, but quite manageable for the 2nd path <br>
But what happens when K>2, 3rd, 4th and more incoming paths

## Slide 32
Raw Signal
Align and Cancel 1st Path
Align and Cancel 3rd Path
Residues
-
-
-
-
-
-
-
Linear Combination
Final Residue
Align and Cancel 2nd Path
Theoretically, residues of all paths
are linearly dependent (proof in the paper)
IAC step K: Compute
Notes: For the next K path, we can find the Kth residue vector, and all the residue vectors will still be linearly dependent.
So theoretically, IAC can find arbitrary number of paths.

## Slide 33
Find : Align and cancel on first few samples
Find : On next few samples after , find , , that minimize the final residue of all paths.
Over-determined: samples decided by variables.
IAC Summary: Find optimal , ,
Notes: This slides conclude of the core algorithm. First, we find the first path AoA by align and cancel on the first few samples, where the second path signal has not arrived.
Second, with the AoA0 determined, we find the AoA for next path by solving jointly solving three variables, the new AoA, path delay delta tk, and path scaler alpha k.
The objective function is the final residue vector after aligning all k paths. Note that this problem is over-determined, because we have many samples from different pause opportunities, and only 3 k variables, where k is the number of paths

## Slide 34
1. A new AoA algorithm
2. Application: voice localization
This paper
Notes: With this new AoA algorithm, let’s see how this can be useful in a voice localization application

## Slide 35
Alexa,
turn on the light
Notes: For example, when you say, Alexa, turn on the light. <br>
It should search the places like<br>
bedroom, living room, kitchen, and study room. <br>
And finally it knows: ah, you’re in the kitchen, and turns on only the kitchen’s light

## Slide 36
Alexa, add “urgent” to groceries
Do you mean “detergent”?
Notes: When you’re in the laundry and say, <br>
Alexa, add “urgent” to groceries.
Of course Alexa knows “urgent” is not a product. Because you’re in the laundry, it will try to make a guess: <br>
Oh, do you mean “detergent”?

## Slide 37
Can Amazon Alexa localize the user from her voice command
Require 2 AoAs
Require wall config
Reverse triangulation
VoLoc Part II: How to find the wall distance/ orientation
Notes: The target is to tell where is the user when Alexa hears the command. <br> Imagine a house where Alexa is using the microphone array <br> and imagine a user giving a voice command <br> When the user speaks, the voice arrives over the line of sight path … as well as echoes that bounce off the walls. VoLoc wants to use these signals to estimate the user’s location. Observe that VoLoc already knows the 2 AoAs of the signals. <br>However, it’s not enough, we need to know where is the wall <br> and then we can do reverse triangulation to locate the user<br>
But how can we know where is the wall?

## Slide 38
VoLoc estimates wall geometry using past voice commands
By assuming one stable wall, models echoes from the wall, and solves a minimization function.
Notes: To find the wall configuration, we run optimization on all past commands. <br>
We models echoes from the wall, and solves a minimization function
<br> we can see that the wall config converges with in just 10 commands.

## Slide 39
Implementation and Evaluation
Notes: At the end, let’s see the VoLoc implementation and evaluation

## Slide 40
6 Microphones
Raspberry Pi
(To obtain raw acoustic samples)
Seeed Studio 6-Mic Circular Mic Array + Raspberry Pi
Notes: Because native Amazon Echo speaker does not provide raw audio samples, we use a 6 mic circular array hat on a raspberry pi to simulate the smart speaker

## Slide 41
Comparison with existing algorithms
VoLoc can improve the AoA estimates of at least 2 echoes
Notes: Comparing with existing algorithms like GCC-PHAT and MUSIC, VoLoc can improve the AoA estimates of at least 2 echoes, and the improvement on the 2nd AoA is substantial

## Slide 42
Median location error: 0.44 meters
Overall location accuracy
Notes: And our system report the median location error of 44 cm in different environments like studio, kitchen, office.

## Slide 43
Location accuracy over clutter level
Notes: We have also tested the algorithm when the speaker is in a clutter environment, meaning there are many objects creating reflections. The performance is affected, but still stable.

## Slide 44
Iterative align and cancel (IAC) algorithm
Indoor user localization from voice signals
Single microphone array (Alexa) as the receiver
Reverse triangulate with few AoAs
Median error < 50cm
VoLoc Summary
Notes: To sum up,
We propose an IAC algorithm to estimate the AoAs of every echoes
And we propose VoLoc, an indoor user localization system using voice signals as the input.
We need a microphone array like Alexa Echo as the receiver, and we use the direct path and the reflected path to do reverse triangulate to localize the user
We can achieve the median positioning error is less than 50cm

## Slide 45
Much more in the paper
Shen
Daguan
Zhijian
Yu-Lin
Romit
Notes: For technical details and more results, please refer to our paper.